## Slide 1
LITERATURE
REVIEW
Medical Thermal
Imaging Technologies
for Breast Cancer & Tumor Detection
Researchers: Lofoga Innocent & Ayikoru Winnie
Objective: To review medical thermal imaging technologies and identify future research directions.
Notes: Good morning everyone. My name is Lofoga Innocent, and together with my research partner Ayikoru Winnie, I'm excited to present our progress on Objective One of our project — a comprehensive literature review of medical thermal imaging technologies for breast cancer and tumor detection.
This literature review forms the scientific foundation of our broader project, which is the development of a low-cost thermal imaging device right here at Mbarara University of Science and Technology. Before we build, we needed to deeply understand what the science says — and that's exactly what this review covers.
Let's get started.

## Slide 2
Introduction & Global Impact
2.1M+
New breast cancer
cases annually
96%
Treatable if caught
before metastasis
#1
Leading cancer
in women worldwide
Why Thermal Imaging?
Conventional screening (mammography, MRI, CT) carries ionizing radiation, high cost, and patient discomfort
Reduced sensitivity in dense breast tissue and limited access in low- & middle-income countries (LMICs)
Digital Infrared Thermal Imaging (DITI): non-invasive, radiation-free, cost-effective complementary modality
Malignant tumors exhibit heightened metabolic activity → measurable surface temperature anomalies
Notes: Let me start by grounding us in why this work matters.
Breast cancer causes over 2.1 million new cases every year globally — it is the number one cancer affecting women worldwide. And here's the heartbreaking truth: research shows that approximately 96% of cancers are treatable if caught before they spread. The problem is not a lack of solutions — it's a lack of accessible, early detection.
Conventional tools like mammography, MRI, and CT scans are effective, but they come with serious limitations — they use ionizing radiation, they're expensive, they're uncomfortable, and in countries like Uganda, they're simply not available to most women.
This is where Digital Infrared Thermal Imaging — or DITI — comes in. It is non-invasive, it produces zero radiation, it's potentially low-cost, and it detects cancer based on a fascinating biological principle: malignant tumors run hotter than healthy tissue. Our device exploits exactly this principle.

## Slide 3
Biological Basis of Thermal Imaging
Tumor Thermobiology
Cancer cells: uncontrolled proliferation + elevated metabolic rates → excess heat
Pennes bioheat transfer equation relates temperature to metabolic heat generation, blood perfusion, and thermal conductivity
Angiogenesis: VEGF-driven new blood vessel growth → increased vascularity → higher local temperatures
Thermal asymmetries of 1–3°C detectable even before tumor is palpable
Thermography can theoretically detect tumors at very early stages
Thermal Signatures by Cancer Type
Breast Cancer: Anterior chest thermal asymmetries; malignant areas appear as elevated temp regions
Thyroid Cancer: Increased intranodular vascularity → elevated skin temp over anterior neck
Skin Cancers: Localized thermal elevations directly on skin surface (melanoma, BCC)
Brain & Rectal: Greater technical complexity due to depth and anatomical barriers
Notes: So why do tumors run hotter? Let me explain the biology behind this.
Cancer cells multiply rapidly and have elevated metabolic rates — this uncontrolled activity generates excess heat. The Pennes bioheat transfer equation — a well-established mathematical model — captures this relationship between metabolic heat, blood flow, and tissue temperature.
There's also a key process called angiogenesis — this is where tumors release growth factors called VEGF, which trigger the formation of new blood vessels to feed the growing tumor. This creates a dense, chaotic vascular network that increases local blood flow and raises local temperature.
The result? Thermal asymmetries of 1 to 3 degrees Celsius on the skin surface — detectable by an infrared camera before the tumor is even large enough to feel.
Different cancers produce different thermal signatures. Breast cancer shows up as hot spots on the chest. Thyroid cancer causes elevated temperatures on the neck. Skin cancers are directly visible on the surface. This biological reality is what makes thermography scientifically credible — and it's the core principle powering our device.

## Slide 4
Medical Thermal Imaging Technologies
Passive (Static) IR
Detects natural body heat. FLIR SC-620 at 640×480px with <0.05°C sensitivity. Prone positioning for multi-angle breast imaging.
Dynamic (Active)
Applies cooling/heating stimulus then tracks tissue thermal response. Cancerous regions show faster thermal recovery due to higher vascularization.
Lock-in (LIT)
Periodic modulated heat + lock-in detection algorithms. Significantly enhances signal-to-noise ratio for skin cancer depth assessment.
Rotational Breast (RBT)
Camera rotates around patient capturing 3D thermal information. Multi-angle comprehensive breast coverage.
Endoscopy (ITME)
Label-free internal tumor detection using anti-reflection Ge lenses. Preclinical rectal tumor detection in mouse models validated.
ICET Imaging
Magnetically induced currents exploit 2.5× higher tumor electrical conductivity. Improves deep lesion detection by 4mm sensitivity.
Notes: The literature describes several distinct thermographic technologies, and our review maps all of them.
The most common is Passive or Static IR thermography — no external stimulation, just capturing the body's natural heat. Modern cameras like the FLIR SC-620 can detect temperature differences as small as 0.05 degrees Celsius. This is the approach closest to what our device uses.
Dynamic or Active thermography goes further — it applies a cooling or heating stimulus and then observes how tissue recovers. Cancerous tissue, with its higher blood supply, recovers faster. This adds discriminatory power.
Lock-in thermography uses periodic heating pulses and signal processing algorithms to dramatically improve the signal-to-noise ratio — very useful for detecting deeper lesions.
Rotational Breast Thermography captures images from multiple angles as the camera rotates around the patient — giving 3D thermal coverage.
ITME — Infrared Thermal Modulation Endoscopy — is a breakthrough for internal tumors. It adapts thermographic principles for endoscopic use, detecting early rectal tumors in preclinical models.
And finally, ICET imaging uses magnetically induced electrical currents to exploit the fact that tumor tissue has 2.5 times higher electrical conductivity than normal tissue — improving detection of deep lesions by 4 millimetres.
Understanding all of these modalities shaped decisions in our hardware and algorithm design.

## Slide 5
Emerging Access Technologies
Smartphone-Based Thermal Imaging
FLIR One Pro — Smartphone-attachable thermal sensor enabling resource-limited clinical settings AI-powered Breast Cancer Pre-Screening Solution (BCPS) demonstrated comparable performance to mammography in first-pass screening High relevance for LMICs where mammography infrastructure is limited — enables community-level cancer screening
AI Integration Advantage
Miniaturized thermal sensors + AI = portable diagnostics accessible outside hospital infrastructure. Democratizes early cancer screening for underserved populations globally.
Notes: One of the most exciting developments in the field — and directly relevant to our project — is the miniaturisation of thermal imaging into smartphone-based devices.
The FLIR One Pro is a smartphone-attachable thermal sensor that has been validated in clinical studies. An AI-powered Breast Cancer Pre-Screening Solution built around this type of sensor demonstrated performance comparable to mammography in first-pass screening.
Why does this matter for us? Because in Sub-Saharan Africa, over 70 percent of breast cancer patients are diagnosed at advanced stages — largely because they simply cannot access a mammogram. A smartphone-based thermal imager changes that equation entirely. It enables community-level screening, outside hospital walls, at a fraction of the cost.
Our device — built around the AMG8833 sensor and NodeMCU ESP8266 — is inspired by exactly this vision: bringing safe, affordable, non-ionizing screening to women in underserved communities right here in Uganda.

## Slide 6
AI & Deep Learning in Thermal Image Analysis
Computer-Aided Diagnosis (CAD) Pipeline
Acquisition
→
Preprocessing
→
Segmentation
→
Feature Extraction
→
Classification
Traditional Machine Learning
SVM, Random Forests, kNN, Naive Bayes, ANN
GLCM, LBP, HOG for texture feature extraction
Statistical features: mean temp, entropy, asymmetry indices
Limitation: expert-designed features may miss complex non-linear thermal patterns
Deep Learning (CNN)
VGG16, ResNet, DenseNet, InceptionV3, EfficientNet via transfer learning
Thermo-CAD multi-CNN system: high accuracy, reduced complexity
PSO-tuned CNN: significantly reduces false positive rates
InceptionV4 applied to real-time thermography video streaming
Notes: Capturing thermal images is only half the challenge. The other half is interpreting them accurately and consistently — and this is where Artificial Intelligence has transformed the field.
A standard Computer-Aided Diagnosis pipeline moves from image acquisition through preprocessing, segmentation, feature extraction, and finally classification. Each stage has been the subject of intense research.
Earlier systems used traditional machine learning — Support Vector Machines, Random Forests, and neural networks — applied to handcrafted image features like texture descriptors and temperature asymmetry indices. These worked reasonably well but were limited by human-designed feature engineering.
The real leap came with deep learning. Convolutional Neural Networks like VGG16, ResNet, and InceptionV3 learn their own features directly from raw image data through transfer learning. The Thermo-CAD system achieved high accuracy with reduced computational complexity. A PSO-optimized CNN significantly reduced false positive rates — which is critical for clinical trust.
For our device, we are incorporating a thermal interpolation algorithm that upscales the raw 8×8 sensor data into a smooth 70×70 heatmap — this is our first step in the image analysis pipeline, and the literature strongly supports this approach as the foundation for further AI integration in future work.

## Slide 7
Applications Across Cancer Types
Breast Cancer
Most extensively investigated — driven by global incidence
Non-invasive, painless, no radiation, no compression required
97–100% diagnostic accuracy in optimized deep learning models
FDA: thermography is adjunct to, not replacement for, mammography
Primary dataset: DMR-IR (Brazil)
Thyroid Cancer
Nodule prevalence up to 65% in adults; most benign
AI + infrared thermography: 91.11% classification accuracy (CNN)
Non-invasive alternative to fine-needle aspiration biopsy
Hybrid ultrasound + thermography models outperform either alone
Skin & Internal Tumors
Melanoma & BCC: localized thermal elevations directly on skin surface
Thermal wave imaging distinguishes melanoma from benign nevi
Brain tumors: intraoperative thermal mapping for margin delineation
Rectal tumors: ITME demonstrated in preclinical mouse models
Notes: The literature review covers thermography applications across multiple cancer types, which demonstrates the breadth and potential of this technology.
Breast cancer dominates the research landscape — and for good reason. Thermography is painless, requires no compression, and produces no radiation. Optimized deep learning models in the literature achieve between 97 and 100 percent diagnostic accuracy. The FDA currently positions thermography as a complementary tool to mammography, not a replacement — and we align with that positioning for our device.
For thyroid cancer, AI-enhanced thermography achieved 91.11 percent classification accuracy using CNN models — offering a non-invasive alternative to fine-needle aspiration biopsy for pre-operative risk stratification.
For skin cancers like melanoma, thermography is particularly powerful because the lesions are right at the surface. Thermal wave imaging has successfully distinguished malignant melanoma from benign skin conditions.
Even internal tumors — brain and rectal — have been explored, with ITME showing early promise in preclinical models. This tells us that the fundamental principle of thermography has far broader applicability than just the breast.

## Slide 8
Current Challenges & Limitations
Clinical Validation
Small single-center datasets; lack of large-scale RCTs; FDA has not approved thermography as primary breast cancer screening tool
Dataset Limitations
Most models trained on DMR-IR alone; poor generalization across cameras, protocols, populations; class imbalance issues
Physiological Confounders
Ambient temperature, menstrual cycle, hormonal contraceptives, caffeine, prior skin treatments all alter thermal signatures
Depth Limitation
Passive IR sensitivity drops for tumors >2–3 cm below skin surface due to tissue insulation; particularly affects larger breasts
Model Interpretability
Black-box CNN decisions not acceptable clinically; XAI methods (Grad-CAM, SHAP) being developed but lack clinical validation
Protocol Standardization
No international standards for room conditions, camera specs, patient preparation, acquisition timing — hinders cross-study comparisons
Notes: No honest review would be complete without confronting the limitations — and there are real ones that we must acknowledge, both for academic rigour and for our own project planning.
The biggest challenge is clinical validation. Most published studies are small and single-centre. The FDA has not approved thermography as a primary screening tool because there are no large-scale randomised controlled trials yet.
Dataset limitations are also significant. Almost all deep learning models in the literature are trained on a single dataset — the DMR-IR database from Brazil. This raises serious questions about whether these models generalise to African populations, different camera hardware, and different clinical protocols — questions directly relevant to our work.
Physiological confounders are real — ambient room temperature, hormonal cycles, caffeine consumption — all of these can alter a thermal signature. This is why our device design includes a controlled measurement protocol.
The depth limitation is a fundamental physical constraint — passive IR cameras cannot reliably detect tumours deeper than 2 to 3 centimetres below the skin surface. This is something we are transparent about in our device specifications.
And finally, AI interpretability remains unsolved. Black-box CNN decisions are not acceptable to clinicians who need to understand why a system flagged a result. Explainable AI methods are being developed, but not yet clinically validated.
These challenges don't undermine the technology — they define the research agenda going forward.

## Slide 9
Future Research Directions
01
Multimodal Fusion
Fuse thermography with mammography, ultrasound, MRI & clinical biomarkers. Studies show 3–7% accuracy gain over single-modality.
02
Federated Learning
Privacy-preserving distributed AI training across institutions without sharing raw patient data. Currently only 1–3 published studies.
03
Protocol Standardization
International standards for room conditions, patient prep, calibration. Especially critical for African populations with limited mammography.
04
Wearable Monitoring
Flexible IR sensors for continuous skin temperature tracking. Integration with smartphone apps for decentralized early detection.
05
Nanoparticle Enhancement
Magnetic nanoparticles as contrast agents. EPR effect → tumor accumulation → magnetic heating → improved deep tumor detectability.
06
Explainable AI + Real-Time Video
Grad-CAM/SHAP overlays for clinician trust. 3D CNNs, ConvLSTMs for spatiotemporal thermographic video analysis.
Notes: Based on this comprehensive review, we identified six high-priority directions that should guide future research — including our own continued work.
First, multimodal fusion — combining thermal images with mammography, ultrasound, or MRI data has shown 3 to 7 percent accuracy improvements. This is a natural extension of our current single-modality approach.
Second, federated learning — this allows multiple hospitals to collaboratively train AI models without sharing raw patient data. With only 1 to 3 published studies in this space, it is an almost completely open research frontier.
Third, protocol standardisation — the field desperately needs international standards for imaging conditions, patient preparation, and data annotation. This is especially urgent for African populations, where we are uniquely positioned to contribute data that the global literature currently lacks.
Fourth, wearable thermal monitoring — flexible infrared sensors that continuously track skin temperature could provide longitudinal data far richer than a single clinic visit.
Fifth, nanoparticle enhancement — magnetic nanoparticles that accumulate in tumours and can be externally heated could extend thermographic sensitivity to deeper lesions — potentially solving the depth limitation.
Sixth, explainable AI and real-time video thermography — spatiotemporal deep learning architectures applied to thermographic video streams represent the next frontier in diagnostic intelligence.
Our device contributes to directions three and four in particular — generating locally-relevant Ugandan data and exploring a portable, community-deployable form factor.

## Slide 10
Conclusion
Thermal imaging is scientifically grounded, radiation-free, and rapidly evolving as a complementary cancer detection modality.
✓ Achievements
Improved IR sensor sensitivity and novel dynamic techniques
CNNs, transfer learning, physics-informed inverse modeling
Application expanded to breast, thyroid, skin, rectal, brain tumors
Smartphone-based democratization for LMICs
⚠ Remaining Challenges
Small, non-diverse datasets; no standardized protocols
No FDA approval as primary screening tool
Physiological confounders in routine clinical practice
Depth limits for deep-seated tumors; AI interpretability
Notes: To conclude — and I want to leave you with a clear message.
Medical thermal imaging is not experimental speculation. It is scientifically grounded in the well-understood thermobiology of malignant tumours. It is supported by decades of research and increasingly sophisticated technology. And it is uniquely positioned to address the cancer detection gap in low-resource settings like ours.
The achievements the field has made are real and significant: improved sensor technology, powerful deep learning models, expanded clinical applications, and the emergence of affordable smartphone-based solutions.
But the challenges are equally real: limited diverse datasets, no standardised protocols, no FDA approval as a primary tool, and unresolved questions about AI interpretability and deep tumour detection.
Our project — the low-cost thermal imaging device being developed right here at MUST — sits precisely at this intersection. We are building a tool that responds to local clinical need, informed by a thorough understanding of global scientific evidence, with the ambition of generating African data that the global literature currently lacks.
Thank you for your time and attention. Ayikoru and I are happy to take any questions.